## Slide 1: Worst-Case Latency Analysis of Message Synchronization in ROS
Ruoxiang LI1, Xu Jiang2, Zheng Dong3, Jen-Ming Wu4,
Chun Jason Xue1, Nan Guan1
1City University of Hong Kong
2Northeastern University
3Wayne State University
4Hon Hai Research Institute
RTSS 2023
44th IEEE Real-Time Systems Symposium
December 5-8, 2023
Taipei

## Slide 2: Sensor Fusion
Widely used in autonomous machines
  Robotics, autonomous vehicles, UAVs…
For example, autonomous vehicles use
  Camera, LiDAR, Radar, GNSS, IMU, …
Picture from The Economist, “How does a self-driving car work?”
A DSP For Implementing High-Performance Sensor Fusion On An Embedded Budget

## Slide 3: Sensor Fusion
Widely used in autonomous machines
  Robotics, autonomous vehicles, UAVs…
For example, autonomous vehicles use
  Camera, LiDAR, Radar, GNSS, IMU, …
Combining sensor data from disparate sources provides information with high precision and less uncertainty
Picture from The Economist, “How does a self-driving car work?”

## Slide 4: Sensor Fusion
Sensor fusion algorithms assume “data from different sensors are sampled at the same time”
Sensor 1
Sensor 2
Sensor 3
Fusion

## Slide 5: Sensor Fusion
Sensor fusion algorithms assume “data from different sensors are sampled at the same time”
However, this assumption rarely holds in reality
  Different sensor sampling frequencies
  Delays before reaching the fusion point
Sensor 1
Sensor 2
Sensor 3
Fusion
Picture from RTSS 2021 Industry Challenge

## Slide 6: Data Synchronization
Add data synchronization before sending them to fusion
Time disparity
  maximal sampling time difference of a set of synchronized data
Sensor 1
Sensor 2
Fusion
Data Sync.
sampling time
Fusion
time
disparity

## Slide 7: Data Synchronization
Add data synchronization before sending them to fusion
Different synchronization policies
Sensor 1
Sensor 2
Fusion
Data Sync.
Apollo Cyber RT
simple policy – always group the newest data
ROS
sophisticated policy – group those with close sampling time
small latency but large time disparity
small time disparity but large latency

## Slide 8: Data Synchronization
Add data synchronization before sending them to fusion
Different synchronization policies
Sensor 1
Sensor 2
Fusion
Data Sync.
sampling time
arrival time
ROS
group messages with close sampling time
delay time

## Slide 9: ROS Synchronization Policy
ROS: the most popular software framework for robotics
In message_filters::sync_policies::ApproximateTime
Applicable to both ROS 1 and 2
Widely used in ROS applications, e.g., Autoware
D. Casini, etc. Response-Time Analysis of ROS 2 Processing Chains Under Reservation-Based Scheduling. ECRTS 2019.
Y. Tang, etc. Response Time Analysis and Priority Assignment of Processing Chains on ROS2 Executors. RTSS 2020.
T. Blass, etc. Automatic Latency Management for ROS 2: Benefits, Challenges, and Open Problems. RTAS 2021.
H. Teper, etc. End-To-End Timing Analysis in ROS2. RTSS 2022.
X. Jiang, etc. Real-Time Scheduling and Analysis of Processing Chains on Multi-threaded Executor in ROS 2. RTSS 2022.
H. Sobhani, ect. Timing Analysis and Priority-driven Enhancements of ROS 2 Multi-threaded Executors. RTAS 2023.
Previous work don’t consider this component.

## Slide 10: Summary of Our Work
Worst-case time disparity analysis
  [1] Worst-Case Time Disparity Analysis of Message Synchronization in ROS. RTSSS 2022.
Formal modeling under limited buffer size
  [2] Modeling and Property Analysis of the Message Synchronization Policy in ROS. MOST 2023.
Worst-case latency analysis
  [3] Worst-Case Latency Analysis of Message Synchronization in ROS. RTSS 2023.

## Slide 11: Technical Contributions of This Work
Study two key latency metrics for ROS message synchronization
  passing latency
  reaction latency
Theoretical upper bounds for both the passing and reaction latency

## Slide 12: Modeling ROS Synchronization Policy
Each message is associated with a timestamp (sampling time)
N input channels, each has an input buffer queue Qi
  Each channel has a minimal/maximal timestamp separation Timin/Timax
  Measage in each channel can experience a minimal/maximal delay time Dimin/Dimax
  Each queue Qi stores arrived messages + a predicted message
    Predicted message’s timestamp = Timestamp of the newest arrived message + Timin
Pivot: the one with largest timestamp among all oldest messages in each Qi
  Pivot must be included in the next published set (sent to fusion point)
timestamp
Q1
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
19
20
21
Q2
Q3
(not arrival time)
T1min
T3min
T2min
pivot
Notes: a predicted message is the last message in each queue
focus on delay!!!!!

## Slide 13: Modeling ROS Synchronization Policy
Selected set
  Includes one message from each channel
  Includes the pivot
  Has the minimal time disparity among all such sets
If selected set has no predicted message, it is published (sent to fusion)
Otherwise, wait, until the selected set is publishable
timestamp
Q1
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
19
20
21
Q2
Q3
(not arrival time)
pivot
T1min
T3min
T2min

## Slide 14: Modeling ROS Synchronization Policy
Selected set
  Includes one message from each channel
  Includes the pivot
  Has the minimal time disparity among all such sets
If selected set has no predicted message, it is published (sent to fusion)
Otherwise, wait, until the selected set is publishable
Publish this publishable selected set, and remove older messages
timestamp
Q1
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
19
20
21
Q2
Q3
T1min
(not arrival time)
T3min
pivot
T2min

## Slide 15: Modeling ROS Synchronization Policy
Selected set
  Includes one message from each channel
  Includes the pivot
  Has the minimal time disparity among all such sets
If selected set has no predicted message, it is published (sent to fusion)
Otherwise, wait, until the selected set is publishable
Publish this publishable selected set, and remove older messages
timestamp
Q1
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
19
20
21
Q2
Q3
(not arrival time)

## Slide 16: Modeling ROS Synchronization Policy
The selected set may turn out to be “wrong”
  A message may have larger timestamp than predicted
timestamp
Q1
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
19
20
21
Q2
Q3
(not arrival time)
T1min
T3min
T2min
Notes: prediction is not always correct.

## Slide 17: Modeling ROS Synchronization Policy
The selected set may turn out to be “wrong”
  A message may have larger timestamp than predicted
In this case, change the selected set
timestamp
Q1
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
19
20
21
Q2
Q3
(not arrival time)
T3min
T2min
T1min

## Slide 18: Modeling ROS Synchronization Policy
The selected set may turn out to be “wrong”
  A message may have larger timestamp than predicted
In this case, change the selected set
timestamp
Q1
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
19
20
21
Q2
Q3
(not arrival time)
T3min
T2min
T1min
This can cause an extra delay time!

## Slide 19: Passing Latency Definition
Passing latency
  the time between when a message arrives and when it is sent out
2
4
6
8
10
12
14
16
18
20
22
24
26
0
channel2
fusion
sensor2
sensor1
channel1
actuator
28
T1min=6
T2min=20
end-to-end delay
passing latency
end-to-end delay
passing latency
synchronzier
arrival time
discarded messages
Notes: It defines the time interval that a message can experience in the synchronizatoin component

## Slide 20: Reaction Latency Definition
Reaction latency
  the time between the arrival of the last message that wasn't discarded and when the message we're focusing on is sent out.
2
4
6
8
10
12
14
16
18
20
22
24
26
0
channel2
fusion
sensor2
sensor1
channel1
actuator
28
event
A
end-to-end reaction time
T1min=6
T2min=20
reaction latency
synchronzier
arrival time
discarded messages

## Slide 21: Reaction Latency Definition
2
4
6
8
10
12
14
16
18
20
22
24
26
0
channel2
fusion
sensor2
sensor1
channel1
actuator
28
event
A
end-to-end reaction time
T1min=6
T2min=20
reaction latency ?
synchronzier
arrival time
Is the difinition correct?
Reaction latency
  the time between the arrival of the last message that wasn't discarded and when the message we're focusing on is sent out.
discarded messages

## Slide 22: Reaction Latency Definition
2
4
6
8
10
12
14
16
18
20
22
24
26
0
channel2
fusion
sensor2
sensor1
channel1
reaction latency
end-to-end reaction time
actuator
28
event
B
We focus on worst-case!
synchronzier
arrival time
Reaction latency
  the time between the arrival of the last message that wasn't discarded and when the message we're focusing on is sent out.
discarded messages
reaction latency
Notes: our interest is to analyze the worst-case end-to-end reaction time no matter when the event actually occurs.
The worst-case scenario is that the external event happens right after the sampling time of the last message that is not discarded

## Slide 23: Passing Latency vs Reaction Latency
arrival time
departure time
Metric | Meaning | End-to-end Metric
Passing latency | time for message going through the synchronizer | E2E delay

## Slide 24: Passing Latency vs Reaction Latency
arrival time
Metric | Meaning | End-to-end Metric
Passing latency | time for message going through the synchronizer | E2E delay
Reaction latency | time for the synchronizer to react to an external signal | E2E reaction time
occurs after the sampling time
of this message

## Slide 25: Passing Latency vs Reaction Latency
departure time
arrival time
Metric | Meaning | End-to-end Metric
Passing latency | time for message going through the synchronizer | E2E delay
Reaction latency | time for the synchronizer to react to an external signal | E2E reaction time

## Slide 26: Passing Latency Analysis - Result 1
Let be any arbitrary output message set. The passing latency experienced by message is upper-bounded by
Theorem 1
Insight: Not only selected messages, but also predicted ones (but unselected) should be waited to arrive.

## Slide 27: Passing Latency Analysis - Result 2
Let be any arbitrary output message set. The passing latency experienced by message is upper-bounded by
Theorem 2
Insight: Not all predicted messages should be waited to arrive.

## Slide 28: Reaction Latency Analysis - Result
Let be any arbitrary output message set published at time . The reaction latency of the message is upper-bounded by
Theorem 3
Insight: Reaction latency is the combination of passing latency and delay time caused by discarded messages.

## Slide 29: Experiments on ROS 2 Humble
Compare theoretical upper-bounds and observed maximum of passing latency under different settings:
  Different number of channels
  Different ratio of maximal and minimal timestamp seperation
  Different delay time experienced by messages before arriving at synchronizer
Passing latency evaluation results

## Slide 30: Experiments on ROS 2 Humble
Compare theoretical upper-bounds and observed maximum of reaction latency under different settings:
  Different number of channels
  Different ratio of maximal and minimal timestamp seperation
  Different delay time experienced by messages before arriving at synchronizer
Reaction latency evaluation results

## Slide 31: Summary
Study two key latency metrics for ROS Synchronization Policy
  passing latency
  reaction latency
Theoretical upper-bounds for both the passing and reaction latency
Experiment verification on ROS 2 Humble
Future work
  Further analysis to reduce the pessimism
  Explore a better evaluation method

## Slide 32
Thanks!
Question?
Ruoxiang LI, PhD Candidate
Email: ruoxiang.li@my.cityu.edu.hk
Supervisor: Prof. Nan Guan